## Slide 1: Sensor Fusion: Ultrasonic Sensor PGA460 and Murata MA58MF14-7N
Summer 2019
Presenter: My Uyen Nguyen, MIT
Mentor: Ankur Deo

## Slide 2: Related Works
On Vehicle
Developed Embedded Platform
Product specs
4 ultrasonic sensors
Up to 2 meters
4 frames per second
1 ultrasonic sensor
Unknown distance range
Unknown feed rate

## Slide 3: Project Objectives
Microcontroller
Ultrasonic Driver
Ultrasonic sensor
Accurate and consistent distance measurement of up to 2 meters
Feed rate of >= 10 frames per second
Multiple sensors configuration using 1 microcontroller

## Slide 4: Challenges and Troubleshooting
Unreliable hardware and software
Failed serial communication and burst+listen
  Constant distance measurement regardless of object detection
  Invalid data transmission
Incomplete understanding of ultrasonic driver’s method of operation
X
X
Microcontroller
Ultrasonic Driver
Ultrasonic sensor

## Slide 5: Method of Operation
BURST + LISTEN
PULL + FILTER DATA
COMPUTE DISTANCE
Loop
INITIALIZATION – EEPROM, Threshold, AFEGAIN + TVG

## Slide 6: Modified Method of Operation
BURST + LISTEN
PULL + FILTER DATA
COMPUTE DISTANCE
1
2
3
Additional Methods of Data Communication
  USB Communication for PC
  CAN Bus for ECUs

## Slide 7: Results
 | Third-Party Device | Inherited Device |  |  | 
Number of sensors | 4 | 1 | 1 | 2 | 3
Min distance (m) | N/A | N/A | 0.25 | 0.25 | 0.25
Max distance (m) | 2.0 | N/A | 3.5 | 3.5 | 3.5
Frames per second | 4 | N/A | 45-50 | 44 | 43
Accuracy | N/A | N/A | +/- .02 | +/- .02 | +/- .02
Developed Embedded System
Performance Comparison

## Slide 8: Future Works
Future Works
Manufacture PCB for multiple-sensors setup (IN PROGRESS)
Test PCB outside of lab and confirm maximum distance range
Install sensors onto vehicle for real-time testing
Increase number of ultrasonic sensors driven by one microcontroller using SoftwareSerial

## Slide 9: Thank you for a wonderful time at KPIT and in India
Special thanks to Ankur Deo and Sant Ranjan